## Slide 1
CH. 7 — WILLIAM STALLINGS, COMPUTER ORGANIZATION AND ARCHITECTURE
Input / Output
Handwritten Lecture Notes — Beginner-Friendly Guide
9 topics · 27 note slides · one keystroke to a mainframe
Computer Architecture — Input / Output — Ch.7, William Stallings

## Slide 2
What we will cover
Today's Notebook — Agenda
Computer Architecture — Input / Output — Ch.7, William Stallings
1.1
External Devices
1.2
I/O Modules
1.3
Programmed I/O
1.4
Interrupt-Driven I/O
1.5
Direct Memory Access
1.6
Direct Cache Access
1.7
I/O Channels & Processors
1.8
External Interconnection Standards
1.9
IBM zEnterprise EC12 I/O Structure

## Slide 3
1.1
Beginner Notes — What is it?
External Devices
Computer Architecture — Input / Output — Ch.7, William Stallings
✎ Simple Definition: Hardware devices outside the CPU and main memory that let the computer interact with the outside world — by taking in data, showing or printing results, or storing data long-term.
Key Points to Remember
Connect through an I/O module — never directly to the CPU
Human-readable: monitor, printer, keyboard
Machine-readable: sensors, disk drives
Communication devices: modem, network card

## Slide 4
1.1
How It Works — Step by Step
External Devices
Computer Architecture — Input / Output — Ch.7, William Stallings
1
You press a key
2
Keyboard creates an electrical signal
3
Signal travels to the I/O module
4
I/O module sends the data to CPU / memory

## Slide 5
1.1
Real-Life Example & Recap
External Devices
Computer Architecture — Input / Output — Ch.7, William Stallings
Picture this: Think of a keyboard like a mailbox — you drop in a letter (a keystroke), and it travels through the postal system (the I/O module) until it reaches the reader (the CPU).
★ QUICK RECAP
External devices are the computer's eyes, ears, hands & mouth — everything it uses to sense and affect the outside world.

## Slide 6
1.2
Beginner Notes — What is it?
I/O Modules
Computer Architecture — Input / Output — Ch.7, William Stallings
✎ Simple Definition: A hardware unit that sits between the CPU/memory and external devices. It manages the messy details of talking to a device so the CPU doesn't have to.
Key Points to Remember
Controls timing so a fast CPU and a slow device can cooperate
Talks to the CPU using commands, status bits and data
Talks to the device using the device's own signals
Buffers data and checks for transmission errors

## Slide 7
1.2
How It Works — Step by Step
I/O Modules
Computer Architecture — Input / Output — Ch.7, William Stallings
1
CPU sends a command
2
I/O module decodes the command
3
Module controls the device directly
4
Module buffers data & reports status back

## Slide 8
1.2
Real-Life Example & Recap
I/O Modules
Computer Architecture — Input / Output — Ch.7, William Stallings
Picture this: An I/O module is like a translator at a meeting — the CPU speaks ‘computer’, the printer speaks ‘printer’, and the translator makes sure both sides understand each other.
★ QUICK RECAP
No device ever connects straight to the CPU — the I/O module is always the middleman.

## Slide 9
1.3
Beginner Notes — What is it?
Programmed I/O
Computer Architecture — Input / Output — Ch.7, William Stallings
✎ Simple Definition: The CPU itself runs the whole I/O operation, checking the device's status again and again until it's ready. This repeated checking is called ‘busy-waiting’.
Key Points to Remember
CPU issues an I/O command to the module
CPU loops, repeatedly testing a status bit
When ready, the CPU transfers the data itself
Very simple to build — but wastes huge amounts of CPU time

## Slide 10
1.3
How It Works — Step by Step
Programmed I/O
Computer Architecture — Input / Output — Ch.7, William Stallings
1
CPU: “Are you ready?”
2
Device: “Not yet”
3
CPU: “Are you ready?” (again …)
4
Device: “Ready!”
5
CPU transfers the data

## Slide 11
1.3
Real-Life Example & Recap
Programmed I/O
Computer Architecture — Input / Output — Ch.7, William Stallings
Picture this: Like standing at the microwave and opening it every 2 seconds to check if your food is hot — instead of doing anything else while you wait.
★ QUICK RECAP
Programmed I/O = the CPU keeps asking ‘are we there yet?’ and can't do anything else meanwhile.

## Slide 12
1.4
Beginner Notes — What is it?
Interrupt-Driven I/O
Computer Architecture — Input / Output — Ch.7, William Stallings
✎ Simple Definition: The CPU starts an I/O operation, then goes back to other work. The device sends an interrupt signal to the CPU only when it's actually ready — no more wasted checking.
Key Points to Remember
CPU issues the command, then keeps running other programs
Device raises an interrupt when it finishes
CPU pauses, saves its state, and runs an interrupt handler
Far more efficient than programmed I/O

## Slide 13
1.4
How It Works — Step by Step
Interrupt-Driven I/O
Computer Architecture — Input / Output — Ch.7, William Stallings
1
CPU starts I/O, then works on other tasks
2
Device finishes and raises an interrupt
3
CPU saves its current state
4
CPU runs the interrupt service routine
5
CPU resumes its earlier work

## Slide 14
1.4
Real-Life Example & Recap
Interrupt-Driven I/O
Computer Architecture — Input / Output — Ch.7, William Stallings
Picture this: Like cooking dinner while waiting for a delivery — instead of standing at the window, you keep cooking, and the doorbell (interrupt) tells you exactly when to answer.
★ QUICK RECAP
Interrupt-driven I/O lets the CPU multitask instead of babysitting the device.

## Slide 15
1.5
Beginner Notes — What is it?
Direct Memory Access
Computer Architecture — Input / Output — Ch.7, William Stallings
✎ Simple Definition: A special DMA controller moves large blocks of data straight between memory and a device, without the CPU handling every byte — freeing the CPU almost completely.
Key Points to Remember
CPU only sets up the transfer: source, destination, length
DMA controller takes over the system bus for the transfer
CPU is free to do other work while the transfer runs
DMA controller interrupts the CPU only once, at the very end

## Slide 16
1.5
How It Works — Step by Step
Direct Memory Access
Computer Architecture — Input / Output — Ch.7, William Stallings
1
CPU tells the DMA controller what to move
2
CPU goes back to other work
3
DMA controller moves data directly (memory ↔ device)
4
DMA controller interrupts CPU: “Done!”

## Slide 17
1.5
Real-Life Example & Recap
Direct Memory Access
Computer Architecture — Input / Output — Ch.7, William Stallings
Picture this: Like hiring a moving crew to carry boxes from the truck into your house — you give them the address, then go back to your own work; they only knock once, when everything is done.
★ QUICK RECAP
DMA removes the CPU from the data path entirely — the biggest efficiency jump in this chapter.

## Slide 18
1.6
Beginner Notes — What is it?
Direct Cache Access
Computer Architecture — Input / Output — Ch.7, William Stallings
✎ Simple Definition: An enhancement where incoming I/O data is placed directly into the CPU's cache instead of main memory first — because the CPU usually needs that data again very soon.
Key Points to Remember
Normal DMA writes to main memory; CPU then fetches it into cache
DCA skips that extra step and writes straight into the cache
Cuts down on cache misses and reduces latency
Especially useful for very fast network I/O

## Slide 19
1.6
How It Works — Step by Step
Direct Cache Access
Computer Architecture — Input / Output — Ch.7, William Stallings
1
Data arrives from a network device
2
Without DCA: memory, then cache (two hops)
3
With DCA: straight into CPU cache (one hop)
4
CPU processes the data immediately

## Slide 20
1.6
Real-Life Example & Recap
Direct Cache Access
Computer Architecture — Input / Output — Ch.7, William Stallings
Picture this: Like a courier placing your package directly on your desk, instead of leaving it in the building’s mailroom for you to walk down and collect.
★ QUICK RECAP
DCA saves a trip — the data lands right where the CPU is about to use it.

## Slide 21
1.7
Beginner Notes — What is it?
I/O Channels & Processors
Computer Architecture — Input / Output — Ch.7, William Stallings
✎ Simple Definition: A separate, small processor dedicated only to managing I/O. It runs its own I/O program and controls many devices, so the main CPU is barely involved at all.
Key Points to Remember
Used in large systems and mainframes with many devices
Selector channel: controls one high-speed device at a time
Multiplexor channel: interleaves many slower devices at once
CPU just starts the channel program, then forgets about it

## Slide 22
1.7
How It Works — Step by Step
I/O Channels & Processors
Computer Architecture — Input / Output — Ch.7, William Stallings
1
CPU starts an I/O channel program
2
Channel processor takes full control of I/O
3
Channel manages many devices independently
4
Channel interrupts the CPU only when the whole job is done

## Slide 23
1.7
Real-Life Example & Recap
I/O Channels & Processors
Computer Architecture — Input / Output — Ch.7, William Stallings
Picture this: Like a CEO who hires an Operations Manager — the manager runs the entire warehouse and staff, and reports back to the CEO only once the big job is finished.
★ QUICK RECAP
I/O channels take delegation even further than DMA — a whole processor devoted just to I/O.

## Slide 24
1.8
Beginner Notes — What is it?
External Interconnection Standards
Computer Architecture — Input / Output — Ch.7, William Stallings
✎ Simple Definition: Agreed-upon rules that let devices from different manufacturers connect to a computer the same way, so almost anything plugs in and just works.
Key Points to Remember
Define the physical connector, signals, and communication rules
Examples: USB, Thunderbolt, PCI Express, SCSI, FireWire
Let one port support many different kinds of devices
Without standards, every device would need a custom connector

## Slide 25
1.8
How It Works — Step by Step
External Interconnection Standards
Computer Architecture — Input / Output — Ch.7, William Stallings
1
A manufacturer builds a device
2
The device follows a shared standard (e.g. USB)
3
Any USB port on any computer accepts it
4
Result: plug-and-play, no custom wiring

## Slide 26
1.8
Real-Life Example & Recap
External Interconnection Standards
Computer Architecture — Input / Output — Ch.7, William Stallings
Picture this: Like a standard wall socket — any lamp, charger, or appliance from any brand can plug in, because everyone agreed on the same socket shape and voltage.
★ QUICK RECAP
Standards are why a random USB drive works on almost any laptop on Earth.

## Slide 27
1.9
Beginner Notes — What is it?
IBM zEnterprise EC12 I/O Structure
Computer Architecture — Input / Output — Ch.7, William Stallings
✎ Simple Definition: The I/O architecture of IBM's zEnterprise EC12 mainframe — built around a Channel Subsystem that manages huge numbers of I/O devices reliably and in parallel.
Key Points to Remember
Channel Subsystem (CSS) fully offloads I/O from the main processors
Multiple independent channel paths can reach the same device
Handles massive I/O throughput for banks, airlines, large enterprises
Built for extreme reliability — a broken path doesn't stop the I/O

## Slide 28
1.9
How It Works — Step by Step
IBM zEnterprise EC12 I/O Structure
Computer Architecture — Input / Output — Ch.7, William Stallings
1
An application requests I/O
2
The Channel Subsystem picks an available path
3
Data moves through that path to the device
4
If a path fails, another path is used automatically

## Slide 29
1.9
Real-Life Example & Recap
IBM zEnterprise EC12 I/O Structure
Computer Architecture — Input / Output — Ch.7, William Stallings
Picture this: Like a large airport with many independent runways — if one runway closes, planes simply use another, and hundreds of flights keep landing safely.
★ QUICK RECAP
This is I/O engineering at mainframe scale — where ‘it must never go down’ is the whole design goal.

## Slide 30
Chapter 7 — The Big Picture
That's a Wrap!
Computer Architecture — Input / Output — Ch.7, William Stallings
The whole chapter is one story: the CPU starts out doing everything itself (Programmed I/O), then hands off more and more work — to interrupts, to a DMA controller, to a full I/O channel processor — so it can spend its time computing instead of waiting.
★ Study tip: for each topic, be able to answer — who is in control, and who tells whom when the job is done?