## Slide 1
INPUT / OUTPUT
My Handwritten Study Notes — Computer Architecture
Chapter 7 — William Stallings, Computer Organization and Architecture
1/30

## Slide 2
Topic 1.1
External Devices
DEFINITION
IN SIMPLE WORDS:
Any hardware outside the CPU and main memory that lets the computer talk to the outside world — for input, output, or both.
KEY POINTS TO REMEMBER
Input devices send data IN (keyboard, mouse, scanner)
Output devices send data OUT (monitor, printer, speaker)
Storage devices keep data for later (hard disk, USB drive)
External Devices
Ch.7 • Stallings, Computer Organization & Architecture
2/30

## Slide 3
Topic 1.1
External Devices
HOW IT WORKS
1
1. Device
User types on a keyboard
2
2. Transducer
Converts the keypress into an electrical signal
3
3. Link/Cable
Signal travels through a cable or wireless link
4
4. I/O Module
Signal reaches the I/O module, ready for the CPU
Rule of thumb: if you can physically touch it and it isn't the CPU or RAM, it's probably an external device!
External Devices
Ch.7 • Stallings, Computer Organization & Architecture
3/30

## Slide 4
Topic 1.1
External Devices
EXAMPLE
REAL-LIFE EXAMPLE
Your USB mouse is an external device. When you move it, it sends tiny electrical signals to the computer telling it how far, and in which direction, to move the cursor on screen.
KEY TAKEAWAY
External devices are the computer's eyes, ears, hands, and voice — its only way to sense and affect the real world.
Remember: external devices = hardware outside CPU/memory used for input and/or output.
External Devices
Ch.7 • Stallings, Computer Organization & Architecture
4/30

## Slide 5
Topic 1.2
I/O Modules
DEFINITION
IN SIMPLE WORDS:
A hardware unit that sits between the CPU/memory (system bus) and an external device, translating and managing the data flow between them.
KEY POINTS TO REMEMBER
Acts like a translator between the CPU and a device
Buffers data — holds it temporarily
Checks for transmission errors
I/O Modules
Ch.7 • Stallings, Computer Organization & Architecture
5/30

## Slide 6
Topic 1.2
I/O Modules
HOW IT WORKS
1
1. Control & Timing
Coordinates data flow with correct timing
2
2. CPU Link
Understands CPU commands: read, write, status
3
3. Device Link
Talks to the device in its own native language
4
4. Buffering
Stores data temporarily since devices are slower
Without an I/O module, the CPU would need to know the tiny electrical details of every single device — that's impossible to manage!
I/O Modules
Ch.7 • Stallings, Computer Organization & Architecture
6/30

## Slide 7
Topic 1.2
I/O Modules
EXAMPLE
REAL-LIFE EXAMPLE
A disk controller card is an I/O module. It takes the CPU's simple request — 'save this file' — and manages exactly how the bits are written onto the spinning disk.
KEY TAKEAWAY
I/O modules hide device complexity from the CPU, so the CPU only deals with simple, standard commands.
Remember: I/O module = the 'middleman' hardware between the CPU/bus and an external device.
I/O Modules
Ch.7 • Stallings, Computer Organization & Architecture
7/30

## Slide 8
Topic 1.3
Programmed I/O
DEFINITION
IN SIMPLE WORDS:
The CPU directly controls the I/O operation: it sends the command and then keeps checking (polling) the device's status until the job is finished.
KEY POINTS TO REMEMBER
CPU issues the command itself
CPU repeatedly asks: 'are you done yet?'
This constant checking is called BUSY-WAITING
Programmed I/O
Ch.7 • Stallings, Computer Organization & Architecture
8/30

## Slide 9
Topic 1.3
Programmed I/O
HOW IT WORKS
1
1. Send Command
e.g., 'print this character'
2
2. Device Starts
Device begins working (often slowly)
3
3. CPU Polls
CPU keeps asking: ready? ready? ready?
4
4. Transfer Data
Once ready, CPU itself moves the data
Simple to build, but very wasteful — a fast CPU sits idle, doing nothing useful, while a slow device finishes its work.
Programmed I/O
Ch.7 • Stallings, Computer Organization & Architecture
9/30

## Slide 10
Topic 1.3
Programmed I/O
EXAMPLE
REAL-LIFE EXAMPLE
Imagine calling a friend and, instead of hanging up, repeating 'are you there yet? are you there yet?' every second until they answer — that wastes your time just like busy-waiting wastes CPU time.
KEY TAKEAWAY
Programmed I/O is the simplest method — but the biggest waste of precious CPU time.
Remember: programmed I/O = CPU sends command, then busy-waits, polling until the device is ready.
Programmed I/O
Ch.7 • Stallings, Computer Organization & Architecture
10/30

## Slide 11
Topic 1.4
Interrupt-Driven I/O
DEFINITION
IN SIMPLE WORDS:
The CPU issues a command and then goes back to doing other useful work. The device 'interrupts' the CPU only when it has finished.
KEY POINTS TO REMEMBER
No busy-waiting — CPU stays productive
Device raises a signal (interrupt) when ready
CPU pauses its task, handles the I/O, then resumes
Interrupt-Driven I/O
Ch.7 • Stallings, Computer Organization & Architecture
11/30

## Slide 12
Topic 1.4
Interrupt-Driven I/O
HOW IT WORKS
1
1. Send Command
CPU issues command, then moves on
2
2. Device Works
CPU is free to run other programs
3
3. Interrupt!
Device sends an 'I'm done!' signal
4
4. Handle & Resume
CPU transfers data, resumes old task
It's like leaving your phone on silent while cooking — you don't keep checking it, but it buzzes (interrupts you) only when a message actually arrives.
Interrupt-Driven I/O
Ch.7 • Stallings, Computer Organization & Architecture
12/30

## Slide 13
Topic 1.4
Interrupt-Driven I/O
EXAMPLE
REAL-LIFE EXAMPLE
While you type on a keyboard, the CPU can run a background download. Each keystroke sends a tiny interrupt so the CPU briefly handles it, then returns to the download.
KEY TAKEAWAY
Interrupt-driven I/O is far more efficient than programmed I/O, since the CPU is never stuck idly waiting.
Remember: interrupt-driven I/O = CPU works freely and is only interrupted when the device is done.
Interrupt-Driven I/O
Ch.7 • Stallings, Computer Organization & Architecture
13/30

## Slide 14
Topic 1.5
Direct Memory Access (DMA)
DEFINITION
IN SIMPLE WORDS:
A special hardware controller (the DMA controller) moves data directly between an I/O device and main memory — without the CPU handling every single byte.
KEY POINTS TO REMEMBER
CPU only sets up the transfer (source, destination, count)
The DMA controller performs the actual copying
CPU is interrupted just ONCE, when it's all done
Direct Memory Access (DMA)
Ch.7 • Stallings, Computer Organization & Architecture
14/30

## Slide 15
Topic 1.5
Direct Memory Access (DMA)
HOW IT WORKS
1
1. CPU Configures
Gives source, destination, byte count
2
2. CPU is Free
Completely free during the transfer
3
3. DMA Transfers
Moves data directly using the bus
4
4. Final Interrupt
'All data transferred!' — just once
DMA removes the CPU from routine, repetitive data-copying jobs — freeing it up for real computation.
Direct Memory Access (DMA)
Ch.7 • Stallings, Computer Organization & Architecture
15/30

## Slide 16
Topic 1.5
Direct Memory Access (DMA)
EXAMPLE
REAL-LIFE EXAMPLE
Copying a large video file from a USB drive to your laptop doesn't freeze your computer — that's DMA quietly doing the heavy lifting in the background.
KEY TAKEAWAY
DMA is the go-to method for large, fast data transfers where CPU involvement would be too costly.
Remember: DMA = a dedicated controller copies data directly to/from memory, bypassing the CPU.
Direct Memory Access (DMA)
Ch.7 • Stallings, Computer Organization & Architecture
16/30

## Slide 17
Topic 1.6
Direct Cache Access (DCA)
DEFINITION
IN SIMPLE WORDS:
An enhancement where incoming I/O data is written directly into the CPU's cache instead of only main memory, so the CPU can use it almost instantly.
KEY POINTS TO REMEMBER
Skips the slow 'memory-then-cache' detour
Reduces latency (delay) for the CPU
Especially useful for high-speed network traffic
Direct Cache Access (DCA)
Ch.7 • Stallings, Computer Organization & Architecture
17/30

## Slide 18
Topic 1.6
Direct Cache Access (DCA)
HOW IT WORKS
1
1. Data Arrives
e.g., a network packet arrives
2
2. Goes to Cache
Placed directly in CPU cache
3
3. CPU Reads Fast
Accesses it instantly from cache
4
4. Fewer Misses
No later fetch from slow memory
DCA is all about SPEED — getting data physically close to the CPU before it's even asked for.
Direct Cache Access (DCA)
Ch.7 • Stallings, Computer Organization & Architecture
18/30

## Slide 19
Topic 1.6
Direct Cache Access (DCA)
EXAMPLE
REAL-LIFE EXAMPLE
It's like a waiter handing your coffee straight to your table (cache) instead of leaving it on a counter across the restaurant (main memory) for you to walk over and fetch.
KEY TAKEAWAY
DCA trades a bit of cache space for a big drop in access latency — great for fast networking.
Remember: DCA = I/O data is placed directly into cache, not just main memory, for faster CPU access.
Direct Cache Access (DCA)
Ch.7 • Stallings, Computer Organization & Architecture
19/30

## Slide 20
Topic 1.7
I/O Channels and Processors
DEFINITION
IN SIMPLE WORDS:
A dedicated, smart processor that runs its own small programs (channel programs) to manage complex I/O completely on its own, without bothering the main CPU.
KEY POINTS TO REMEMBER
More powerful than a simple DMA controller
Can manage MULTIPLE devices at the same time
Common in large mainframe computers
I/O Channels and Processors
Ch.7 • Stallings, Computer Organization & Architecture
20/30

## Slide 21
Topic 1.7
I/O Channels and Processors
HOW IT WORKS
1
1. Selector Channel
Controls one high-speed device
2
2. Multiplexor Ch.
Handles many slow devices together
3
3. I/O Processor
Runs its own program to manage I/O
4
4. CPU Stays Free
Told only when the whole job ends
Evolution ladder: Programmed I/O → Interrupts → DMA → I/O Channels — each step frees the CPU a little more.
I/O Channels and Processors
Ch.7 • Stallings, Computer Organization & Architecture
21/30

## Slide 22
Topic 1.7
I/O Channels and Processors
EXAMPLE
REAL-LIFE EXAMPLE
Think of a hotel manager (I/O processor) who independently coordinates housekeeping, room service, and check-ins — the hotel owner (CPU) doesn't micromanage every task.
KEY TAKEAWAY
I/O channels/processors offload entire I/O programs, ideal for mainframes juggling huge amounts of traffic.
Remember: I/O channel/processor = a smart, independent unit that runs whole I/O programs on its own.
I/O Channels and Processors
Ch.7 • Stallings, Computer Organization & Architecture
22/30

## Slide 23
Topic 1.8
External Interconnection Standards
DEFINITION
IN SIMPLE WORDS:
Agreed-upon rules (protocols) and physical connectors that let devices from ANY manufacturer connect to a computer and work correctly together.
KEY POINTS TO REMEMBER
Ensures compatibility between different brands
Defines cables, connectors, speed, and signaling
Examples: USB, SATA, PCIe, Thunderbolt, FireWire
External Interconnection Standards
Ch.7 • Stallings, Computer Organization & Architecture
23/30

## Slide 24
Topic 1.8
External Interconnection Standards
HOW IT WORKS
1
1. USB
Universal Serial Bus — keyboards, drives, phones
2
2. SATA
Connects internal hard drives & SSDs
3
3. PCIe
High-speed internal expansion cards
4
4. Thunderbolt
Very high-speed data + display + power
Standards are exactly why you don't need a different plug shape for every single brand of device.
External Interconnection Standards
Ch.7 • Stallings, Computer Organization & Architecture
24/30

## Slide 25
Topic 1.8
External Interconnection Standards
EXAMPLE
REAL-LIFE EXAMPLE
Any USB flash drive — from any company — works in any USB port on any laptop, because every manufacturer follows the same agreed USB standard.
KEY TAKEAWAY
Interconnection standards are what make 'plug and play' possible across an entire industry.
Remember: interconnection standards = shared rules that make devices from any vendor compatible.
External Interconnection Standards
Ch.7 • Stallings, Computer Organization & Architecture
25/30

## Slide 26
Topic 1.9
IBM zEnterprise EC12 I/O Structure
DEFINITION
IN SIMPLE WORDS:
A real, large-scale example of enterprise I/O design used in IBM mainframes — built for extreme reliability, redundancy, and non-stop throughput.
KEY POINTS TO REMEMBER
Uses a Channel Subsystem to manage all I/O
Many redundant Channel Paths, so one failure isn't fatal
Designed so banks and airlines never lose critical data
IBM zEnterprise EC12 I/O Structure
Ch.7 • Stallings, Computer Organization & Architecture
26/30

## Slide 27
Topic 1.9
IBM zEnterprise EC12 I/O Structure
HOW IT WORKS
1
1. Channel Subsystem
Central manager of all I/O activity
2
2. Channel Paths
Several routes to reach the same device
3
3. Control Units
Connect channels to storage devices
4
4. Redundancy
A failed path auto-reroutes traffic
This is where every earlier concept — I/O modules, DMA, channels — comes together at massive, real-world scale.
IBM zEnterprise EC12 I/O Structure
Ch.7 • Stallings, Computer Organization & Architecture
27/30

## Slide 28
Topic 1.9
IBM zEnterprise EC12 I/O Structure
EXAMPLE
REAL-LIFE EXAMPLE
A bank's ATM network can run on mainframes like the zEnterprise EC12, so that even if one cable or path fails, your money transfer still goes through safely.
KEY TAKEAWAY
Enterprise mainframe I/O is built around one idea: redundancy, so no single failure stops the system.
Remember: zEnterprise EC12 = a real mainframe using a redundant Channel Subsystem for non-stop I/O.
IBM zEnterprise EC12 I/O Structure
Ch.7 • Stallings, Computer Organization & Architecture
28/30

## Slide 29
QUICK RECAP
SUMMARY
1.1
External Devices
external devices = hardware outside CPU/memory used for input and/or output.
1.2
I/O Modules
I/O module = the 'middleman' hardware between the CPU/bus and an external device.
1.3
Programmed I/O
programmed I/O = CPU sends command, then busy-waits, polling until the device is ready.
1.4
Interrupt-Driven I/O
interrupt-driven I/O = CPU works freely and is only interrupted when the device is done.
1.5
Direct Memory Access (DMA)
DMA = a dedicated controller copies data directly to/from memory, bypassing the CPU.
1.6
Direct Cache Access (DCA)
DCA = I/O data is placed directly into cache, not just main memory, for faster CPU access.
1.7
I/O Channels and Processors
I/O channel/processor = a smart, independent unit that runs whole I/O programs on its own.
1.8
External Interconnection Standards
interconnection standards = shared rules that make devices from any vendor compatible.
1.9
IBM zEnterprise EC12 I/O Structure
zEnterprise EC12 = a real mainframe using a redundant Channel Subsystem for non-stop I/O.
Recap
Ch.7 • Stallings, Computer Organization & Architecture
29/30

## Slide 30
REFERENCES & NEXT STEPS
TEXTBOOK
William Stallings — Computer Organization and Architecture, Chapter 7: Input/Output (pages 230–266).
Sections covered: External Devices · I/O Modules · Programmed I/O · Interrupt-Driven I/O · DMA · Direct Cache Access · I/O Channels & Processors · External Interconnection Standards · IBM zEnterprise EC12 I/O Structure.
Study tip: cover the CPU-involvement ladder — Programmed I/O (CPU fully busy) → Interrupts (CPU checks less) → DMA (CPU barely involved) → I/O Channels (CPU almost free). Knowing WHY each was invented helps you remember the order!
References
Ch.7 • Stallings, Computer Organization & Architecture
30/30