## Slide 1: Computer Architecture CSC-250
COURSE LECTURE
COMPUTER SCIENCE DEPARTMENT
SIBAU KANDHKOT CAMPUS

## Slide 2: Computer Architecture
A very good example of computer architecture is von Neumann architecture, which is still used by most types of computers today.
This was proposed by the mathematician John von Neumann in 1945. It describes the design of an electronic computer with its CPU, which includes the arithmetic logic unit, control unit, registers, memory for data and instructions, an input/output interface and external storage functions
Involves Logics (instruction address data types memory optimization)
Show responsibility who does interconnect & connectivity structure
Functional requirements
High level design
Focus on understanding problem

## Slide 3: Computer Architecture
A modern computer is an electronic, digital, general purpose computing machine that automatically follows a step-by-step list of instructions to solve a problem. This step-by step list of instructions that a computer follows is also called an algorithm or a computer program.
Why study computer organization and architecture?
  Design better programs, including system software such as compilers, operating systems, and device drivers.
  Optimize program behavior.
  Evaluate (benchmark) computer system performance.
  Understand time, space, and price tradeoffs.
Computer organization
  Encompasses all physical aspects of computer systems.
  E.g., circuit design, control signals, memory types.
  How does a computer work?

## Slide 4: Computer Architecture
Visible attributes of system to programmer
System competitive techniques for addressing design
Structural behavior
Instruction Set Architecture (ISA): This is the embedded programming language of the central processing unit.
It defines the CPU's functions and capabilities based on what programming it can perform or process.
This includes the word size, processor register types, memory addressing modes, data formats and the instruction set that programmers use.
Microarchitecture: Otherwise known as computer organization, this type of architecture defines the data paths, data processing and storage elements, as well as how they should be implemented in the ISA.

## Slide 5: Computer Architecture
Focuses on the structure (the way in which the components are interrelated) and behavior of the computer system and refers to the logical aspects of system implementation as seen by the programmer
Computer architecture includes many elements such as
  instruction sets and formats, operation codes, data types, the number and types of registers, addressing modes, main memory access methods, and various I/O mechanisms.
The architecture of a system directly affects the logical execution of programs.
The computer architecture for a given machine is the combination of its hardware components plus its instruction set architecture (ISA).
The ISA is the interface between all the software that runs on the machine and the hard
Studying computer architecture helps us to answer the question: How do I design a computer?

## Slide 6: Computer Architecture Layer
The term layer with regard to computer architecture typically represents the way abstraction is used to describe computer systems.
A layer is the term used to describe the different levels at which you can place an object.
There are many different abstractions that have been used in computer architecture.
If you restricted yourself to four layers, they may be defined as:
1) algorithm,
2) programming language/compiler,
3) processor/memory,
4) I/O.

## Slide 9: Design
This includes all hardware components in the system, including data processors aside from the CPU, such as the graphics processing unit and direct memory access.
It also includes memory controllers, data paths and miscellaneous things like multiprocessing and virtualization.
Develop system components
Understand configuration
Hardware design

## Slide 10: Why We Study Computer Architecture
The study of computer architecture and organization focuses on the interface between hardware and software, and emphasizes the structure and behavior of the system.
As computer users, we probably do not have to worry about this anymore than we need to know what our cars look like under the hood in order to drive them.
We can certainly write high label language programs without understanding how these programs execute.
We can use various application packages without understanding how they really work. But what happens when the program we have written needs to be faster and more efficient or the application we are using does not do precisely what we want?
As Computer Scientists, we need a basic understanding of computer system itself in order to rectify these problems.

## Slide 11: Computer Architecture & Organization
Architecture is those attributes visible to the programmer
  Instruction set, number of bits used for data representation, I/O mechanisms, addressing techniques.
  e.g. Is there a multiply instruction?
Organization is how features are implemented
  Control signals, interfaces, memory technology.
  Organization differs between different versions
  e.g. Is there a hardware multiply unit or is it done by repeated addition?

## Slide 12: Structure
A hierarchical set of interrelated sub system
At each level system is consist of a set of components
The way in which the components are interrelated
Internal structure of a digital computer, encompassing the design and layout of its instruction set and storage registers.
Top to Bottom
Bottom to Top

## Slide 13: Computer Organization Vs Architecture
Computer organization refers to the operational units and their interconnections that realize the architectural specifications.
Computer architecture refers to those attributes of a system visible to a programmer or, put another way, those attributes that have a direct impact on the logical execution of a program.

## Slide 14: Computer Organization includes………
Realization of a hardware
Organization is how features are implemented
    Hardware details – Such as RAM, Hard drive , graphic card technology used.
    Peripherals Devices – How devices such as mouse and keyboard, connected to the computer.
    Control signals. Generating from above mentioned controls

## Slide 15: Computer architecture includes……..
Instruction set, number of bits used for data representation, I/O mechanisms, addressing techniques.
  Physical memory – Allocated and Available
  ISA (Instruction Set Architecture) of the processor.
  The number of bits used to represent data types like integer , character , double etc.
  Input Output mechanism – Depends on programming language.
  Technique for addressing memories – Depends on programming language

## Slide 16: Concept of computer ‘Family’
A computer family is a category of computers with similar designs and microprocessors that are compatible.
Good examples of different computer families are the IBM or PC family versus the Apple or Mac family of computers
Mostly, all computer families have successive generations, they do share the same architecture. But there are always exceptions

## Slide 17: Structure Vs Function
Computer is a complex system with millions of elementary electronic components. How can one describe them?
  Key is to recognize the hierarchical nature of the system
At each level of hierarchy designer is concerned with two things:
  Structure: the way in which components relate to each other
  Function: the operation of individual components as part of the structure

## Slide 18: Functions of Computer
Data processing
    Sorting
    Arithmetic
Data movement
    Moving data to directly connected device, known as I/O
    Moving data to remote device, known as Data Communication
Data storage
    Must be able to store data
    Even if data is processed on fly
    Short term storage, Long term storage
Control
    Programmers control these functions by providing instructions
    Control unit manages the resources in response to those instructions

## Slide 19: Functional View

## Slide 20: Data movement

## Slide 21: Storage

## Slide 22: Processing
(From or To Storage)

## Slide 23
Processing
(From or To I/O)

## Slide 24: Structure - Top Level (Four main structural Components)
Computer
Main
Memory
Input
Output
Systems
Interconnection
Peripherals
Communication
lines
Central
Processing
Unit
Computer
There may be one or more of each of these components

## Slide 25: Structure - The CPU
Computer
Arithmetic
and
Login Unit
Control
Unit
Internal CPU
Interconnection
Registers
CPU
I/O
Memory
System
Bus
CPU

## Slide 26: Structure - The Control Unit
CPU
Control
Memory
Control Unit
Registers and
Decoders
Sequencing
Logic
circuit
Control
Unit
ALU
Registers
Internal
Bus
Control Unit

## Slide 27: The Control Unit
A sequence logic circuit type of logic circuit whose output depends not only on the present value of its input signals but on the sequence of past inputs, the input history as well.
A Control Memory is the storage in the microprogrammed control unit to store the microprogram. Writeable Control Memory: Control Storage whose contents can be modified, allow the change in microprogram and Instruction set can be changed or modified is referred as Writeable Control Memory.
A Control Unit typically uses Registers and Decoders to hold and convert coded instructions into timing and control signals that direct the operation of the other units (memory, arithmetic logic unit and input and output devices, etc.).

## Slide 28: Assignment – 1
Is hard disk a peripheral device?
Why or why not?
Is there a hardware multiply unit or is it done by repeated addition?
Explain by writing a sample program?

## Slide 29: Parts of Computer Hardware
Input
Devices
Output
Devices
Ports
Microprocessor
Memory Unit (RAM, ROM, Cache)
STORAGE DEVICES
(Hard Disk, CD Drive, DVD Drive, Floppy Drive etc.)
Extended Slots
Power
Supply
BUS
BUS
BUS
BUS
BUS

## Slide 30: Year : 300 B.C
ABACUS

## Slide 31: Modern Abacus
Note how the abacus is really just a representation of the human fingers: the 5 lower rings on each rod represent the 5 fingers and the 2 upper rings represent the 2 hands.

## Slide 32: Year : 1617 A.D
Logarithms:
John Napier invented logarithms, which
are a technology that allows multiplication
to be performed via addition.

## Slide 33: Napier’s Bones
The logarithm of each operand was originally obtained from a printed table, but Napier bones were alternative to tables, where the logarithm values were carved on ivory sticks .

## Slide 34: Year : 1642 A.D
Blaise Pascal, at age 19, invented the Pascaline as an aid for his father who was a tax collector.
Up until the present age when car dashboards went digital, the odometer portion of a car's speedometer used the very same mechanism as the Pascaline to increment the next wheel after each full revolution of the prior wheel.

## Slide 35
Just a few years after Pascal, the German Gottfried Wilhelm
Leibniz (co-inventor with Newton of calculus) managed to build a
four-function (addition, subtraction, multiplication, and division)
calculator that he called the stepped reckoner because, instead
of gears, it employed fluted drums having ten flutes arranged
around their circumference in a stair-step fashion.
Although the stepped reckoner employed the decimal number
system (each drum had 10 flutes), Leibniz was the first to
advocate use of the binary number system which is fundamental
to the operation of modern computers. Leibniz is considered one
of the greatest of the philosophers but he died poor and alone.

## Slide 36: Year: 1801 A.D (Punch Cards)
The Frenchman Joseph Marie
Jacquard invented a power
loom that could base its weave
(and hence the design on the
fabric) upon a pattern
automatically read from
punched wooden cards, held
together in a long row by rope.

## Slide 37: Punch card or Jacquard card
A closer look

## Slide 38: Year : 1822 A.D
The English mathematician Charles Babbage was proposing a steam driven calculating machine the size of a room, which he called the Difference Engine. This machine would be able to compute tables of numbers, such as logarithm tables.

## Slide 39: The Difference Engine
A small section of the type of mechanism employed in Babbage's Difference Engine [photo © 2002 IEEE]

## Slide 40: Analytical Engine
This device, large as a house and powered by 6 steam engines, would be more general purpose in nature because it would be programmable, thanks to the punched card technology of Jacquard.
In the Jacquard loom, the presence or absence of each hole in the card physically allows a colored thread to pass or stops that thread (you can see this clearly in the earlier photo). Babbage saw that the pattern of holes could be used to represent an abstract idea such as a problem statement or the raw data required for that problem's solution. Babbage saw that there was no requirement that the problem matter itself physically pass thru the holes.

## Slide 41: Analytical engine (ctd...)
Furthermore, Babbage realized that punched paper could be employed as a storage mechanism, holding computed numbers for future reference. Because of the connection to the Jacquard loom, Babbage called the two main parts of his Analytic Engine the "Store" and the "Mill", as both terms are used in the weaving industry. The Store was where numbers were held and the Mill was where they were "woven" into new results. In a modern computer these same parts are called the memory unit and the central processing unit (CPU).

## Slide 42: Year : 1890 A.D
Herman Hollerith's invention, known as the Hollerith desk, consisted of a card reader which sensed the holes in the cards, a gear driven mechanism which could count (using Pascal's mechanism which we still see in car odometers), and a large wall of dial indicators (a car speedometer is a dial indicator) to display the results of the count.

## Slide 43: Hollerith desks still exist today

## Slide 44: Hollerith and IBM
Incidentally, the Hollerith census machine was the first machine to ever be featured on a magazine cover.
Hollerith built a company, the Tabulating Machine Company which, after a few buyouts, eventually became International Business Machines, known today as IBM. IBM grew rapidly and punched cards became ubiquitous.

## Slide 45: More about IBM
IBM continued to develop mechanical calculators for sale to businesses to help with financial accounting and inventory accounting.
One early success was the Harvard Mark I computer which was built as a partnership between Harvard and IBM

## Slide 46: First Generation - 1940-1956
Major Innovation – Vacuum Tube
The first computers used vacuum tubes and were often enormous, taking up entire rooms.
They were very expensive to operate and in addition to using a great deal of electricity, generated a lot of heat, which was often the cause of malfunctions.
The UNIVAC and ENIAC computers are examples of first-generation computing devices.

## Slide 47: Mark 1

## Slide 48: Mark 1
This was the first programmable digital computer made in the U.S.
It was not a purely electronic computer. Instead the Mark I was constructed out of switches, relays, rotating shafts, and clutches.
The machine weighed 5 tons, incorporated 500 miles of wire, was 8 feet tall and 51 feet long, and had a 50 ft rotating shaft running its length, turned by a 5 horsepower electric motor.
The Mark I ran non-stop for 15 years, sounding like a roomful of ladies knitting.

## Slide 49: History of ‘Bug’
One of the primary programmers for the Mark I was a woman, Grace Hopper.
Hopper found the first computer "bug": a dead moth that had gotten into the Mark I and whose wings were blocking the reading of the holes in the paper tape.
The word "bug" had been used to describe a defect since at least 1889 but Hopper is credited with coining the word "debugging" to describe the work to eliminate program faults.

## Slide 50: Year : 1943 – 1945
The first electronic digital computer ENIAC (Electronic Numerical Integrator and Calculator)
ENIAC was built by two professors, John Mauchly and J. Presper Eckert at the University of Pennsylvania

## Slide 51: Second Generation - 1956-1963:
Major Innovation – Transistor
The transistor was far superior to the vacuum tube, allowing computers to become smaller, faster, cheaper, more energy-efficient and more reliable than their first-generation predecessors.
Though the transistor still generated a great deal of heat that subjected the computer to damage, it was a vast improvement over the vacuum tube. Second-generation computers still relied on punched cards for input and printouts for output.
The first computers of this generation were developed for the atomic energy industry.

## Slide 52: Third Generation - 1964-1971
Major Innovation – Integrated Circuits / IC
The development of the Integrated Circuits was the hallmark of the third generation of computers.
Transistors were miniaturized and placed on semi conductor chips, called IC, which drastically increased the speed and efficiency of computers.
Instead of punched cards and printouts, users interacted with third generation computers through keyboards and monitors and interfaced with an operating system
Computers for the first time became accessible to a mass audience because they were smaller and cheaper than their predecessors

## Slide 53: Revolution of IC

## Slide 54: Fourth Generation - 1971-Present
Major Innovation – Microprocessor
Microprocessor is defined as thousands of integrated circuits were built onto a single silicon chip.
In 1981 IBM introduced its first computer for the home user
In 1984 Apple introduced the Macintosh.
As these small computers became more powerful, they could be linked together to form networks, which eventually led to the development of the Internet.

## Slide 55: Fifth Generation - Present and Beyond
Major Innovation – Artificial Intelligence
Computers with intelligence like a human being
  Robotics
  Speech and Voice Recognition
  Image and Thumb recognition
  Simulation
  Virtual Reality
  Expert Systems
  Etc.

## Slide 56: The Microprocessor
A combination of integrated circuit that contains all the functions of a central processing unit of a computer.

## Slide 57: Parts of Microprocessor
Control Unit
  A control unit or CU is circuitry that directs operations within a computer's processor. It lets the computer's logic unit, memory, as well as both input and output devices know how to respond to instructions received from a program.
Arithmetic & Logical Unit
  An arithmetic logic unit (ALU) is a digital circuit used to perform arithmetic and logic operations. It represents the fundamental building block of the central processing unit (CPU) of a computer.
Memory Unit / Registers

## Slide 58: Registers
A processor register (CPU register) is one of a small set of data holding places that are part of the computer processor.
A Program Counter / Instruction register hold an instruction
An Address register holds memory addresses
An Accumulator / Data register hold results of frequent calculations within microprocessor

## Slide 59: Memory
Computer memory is any physical device capable of storing information by computer
Volatile memory is computer memory that requires power to maintain the stored information. (e.g. RAM, Cache, Register)
Non-volatile memory is computer memory that can retain the stored information even when not powered. (e.g. ROM, CMOS)

## Slide 60: RAM
Random-access memory is the most common type of memory that stores data and applications currently being used or in execution by computer system. Most modern semiconductor volatile memory is either Static RAM or Dynamic RAM.
DRAM, or Dynamic RAM, is the most widely used RAM that consumers deal with. DDR3 is an example of DRAM. It needs to be refreshed periodically when in use,
SRAM does not need to be refreshed by microprocessor.

## Slide 61: Cache Memory
The cache memory lies in the path between the processor and the memory. So, it is very near to the CPU and also called CPU memory, all the Recent Instructions are Stored into the Cache Memory.

## Slide 62: Cache Memory Types
L1 cache, or primary cache, is extremely fast but relatively small, and is usually embedded in the processor chip as CPU cache.
L2 cache, or secondary cache, is larger than L1. L2 cache may be embedded on the CPU, or it can be on a separate chip.
Level 3 (L3) cache is specialized memory developed to improve the performance of L1 and L2. Also called as external cache.

## Slide 63: ROM and Types
ROM stands for Read Only Memory. The memory from which we can only read but cannot write on it. This type of memory is non-volatile. The information is stored permanently in such memories during manufacture. A ROM stores such instructions that are required to start a computer.
PROM (programmable ROM) is a one - time user-programmable memory.
EPROM (erasable programmable ROM) was invented to allow making changes in the contents of PROM after it is burned.

## Slide 64: ROM and Types
EEPROM (Electrically erasable PROM) does not require the entire contents of ROM are erased. However, the main advantage of EEPROM is that one can program and erase its contents while it is still in the system board. it does not require physical removal of the memory chip from its socket. In other words, unlike UV-EPROM, EEPROM does not require an external erasure and programming device.
4. Flash memory is used to store flexible boot instructions. It allows erasure of the entire contents takes less than a second, or one might say in a flash, hence its name, Flash memory.

## Slide 65: CMOS
CMOS is short for complementary metal-oxide semiconductor.
CMOS is an on-board, battery powered semiconductor chip inside computers.
CMOS generally stores date/time or BIOS passwords information.

## Slide 66: Computer Bus
A bus is a subsystem that is used to connect computer components and transfer data between them.
A System Bus connects microprocessor with RAM while, the control bus a set of connections among the parts in the computer.
The data bus acts as a channel for data from the keyboard, memory and other devices. It passes information at speeds up to billions of characters per second.
The computer must be able to access every character of memory rapidly, so every character has its own address number. The address bus carries such memory addresses.